SKILL TEST NOTES


Perf TakeOff		10° Flap Max runway use. 
			Airborne ASAP in GND effect

Steep Turns 		45° &  60 °
Spiral recovery 	Close Throttle, Level Wings
			ease out of dive

STALLS	SSR: 	Control FWD + FULL Power

(Wings Level until unstalled)

Recovery at: 	1 Instructor Command

2 A/C Stall

3 First sign of Stall

FLWOP 	1 Best Glide

2 Pick Field, 1000’ point, plan.

3 What’s gone wrong? MFI (+Carb Ht)

4 Mayday (How 2 describe pos’n)

5 Crash Check  MFI + HH

Normal Approach	Ask 20° or 30° flap required

Glide Approach		You cut power when you judge 
			you can reach 1/3 in to field.

Use FLAP last!

Flapless Approach	Low aspect approach.  70 KT 
			(High nose attitude)

Short Field		Low aspect approach

30° Flap    55 KT  (in calm air)

NAV TEST

FIX POSITION WITH ONE VOR:

1  Tune to VOR1 – Get Bearing QDR
	(Centre L/R with FROM  flag showing)

2  TURN A/C to Maintain Radial (or QDM)

3  Tune to VOR2 – Get Bearing QDR
	(Centre L/R with FROM  flag showing)

4  Note TIME

5  Plot Bearings on Map.

(Position at Time of VOR2 reading)

DIVERSION

1  Pick Point ahead to Divert from.

2  Plot Track on Map & Estimate NEW Heading

..  Estimate Distance & ETA (may be done after Turning)

3  TURN for Diversion, Note TIME.

GST    Skill Test

Passenger care

Mass & Balance calcs.

General

S&L with speed changes

Climbing:   at best ROC, Turns, Level Off

Medium 30° turns

Steep Turns 360°  L & R  45° bank  + Spiral Dive Recovery

Slow Flight with & without Flap

Clean Stall recovery with Power

Approach to Stall in 20° banked turn

Approach to Stall in Landing configuration

Descending:  Glide & Cruise, Turns (incl. Steep Gliding), Level off

AGA

Arrival Procedure

Short Field, Crosswind, Flapless (as appropriate)

Glide Approach

Touch & Go

Go Round from Low Height

Emergency Procedures

EFATO

Precautionary Landing

Simulated Emergencies

NFT     Navigation Flight Test

Flight Planning incl. Wx

In flight recording (notes on map are acceptable)

ATC liaison

DR Nav:  Correction of track, Revised ETA, DI setting etc.

Map Reading:  (Track crawling not acceptable)

Diversion  - simulated adverse Wx

IMC MINIMA

Precision Approach System Minima

ILS  							200 ft
LPV  (GNSS with SBAS) 				200 ft
Non-Precision Approaches System Minima
LLZ (Localizer only), VOR/DME			250 ft
LNAV, LNAV/VNAV (GNSS Lateral Nav)	250 ft
SRA (terminating 0.5 nm)				250 ft

VOR, NDB/DME					300 ft
SRA  (terminating 1 nm)				300 ft
NDB, VDF (QDM or QGH)				350 ft
SRA (terminating 2+ nm)				350 ft

IMC MINIMA

Precision Approach System Minima

ILS  							200 ft
LPV  (GNSS with SBAS) 				200 ft
Non-Precision Approaches System Minima
LLZ (Localizer only), VOR/DME			250 ft
LNAV, LNAV/VNAV (GNSS Lateral Nav)	250 ft
SRA (terminating 0.5 nm)				250 ft

VOR, NDB/DME					300 ft
SRA  (terminating 1 nm)				300 ft
NDB, VDF (QDM or QGH)				350 ft
SRA (terminating 2+ nm)				350 ft

| Aeroplane Category A, B, C, D ? |
| --- |
| OCH |  |  | Compare ( ( |  |  | SYSTEM Minima |
| Precision Approach add 50 ft PEC |  | +50 ft |  |  |  |
| = Instrument Rating Minima | = |  |  |  |  |
| IMC rating addition |  | +200 ft |  |  |  |
|  | = |  |  | IMC Absolute Minima |
|  |  |  |  |  | Precision App DH 500 ft |
|  |  |  |  | Non-Precision MDH 600 ft |

SKILL TEST Self-Briefing Checklist


Stall  Recovery:      Controls Forward & FULL Power
			(No aileron until un-stalled)

| Recover ON: | 1 Instructor command |
| --- | --- |
|  | 2 A/C Stalls |
|  | 3 First sign of approaching stall |

Forced Landing Without Power

| 1 | Best Glide |
| --- | --- |
| 2 | Pick Field & 1000 ft point, Plan circuit. |
| 3 | What’s gone wrong? MFI (Carb Heat) |
| 4 | Mayday (How 2 describe position) |
| 5 | Crash Checks MFI + H H |

Glide Approach

Cut power when you judge you can reach 1/3 in to field

Use Flap LAST in stages.

Flapless Approach

Low aspect approach (extend downwind)

Expect high nose attitude

Short Field Landing
	Low aspect approach.

30° Flap,   55 Kt (in calm air)

|  | 10° flap |
| --- | --- |
|  | Max Runway use |
|  | Airborne ASAP (in Ground effect) |

Performance Take-Off

Normal Approach

20° or 30° Flap AS required.


Spiral Recovery

|  | Close Throttle |
| --- | --- |
|  | Level Wings |
|  | Ease out of dive |

Nav Diversion

| 1 | Pick point ahead to divert from |
| --- | --- |
| 2 | Plot Track, Estimate New Heading |
|  | Estimate Distance & ETA |
|  | Turn for diversion. Note Time. |

Radio Nav Position Fix

| 1 | Get Bearing from VOR1 (Centre L/R with FROM flag showing) |
| --- | --- |
| 2 | Turn A/C to maintain bearing (QDR or QDM) |
| 3 | Get Bearing from VOR2 (Centre L/R with FROM flag showing) |
| 4 | Note time X |
| 5 | Plot Bearings on map (= position at time X) |

# Text boxes

OCH
for A/C Group

Compare

For Precision Approach
+50ft Alt P.E.C.
(nil correction for Non-Precision)